## Slide 1
PBS 16 Numbering System
Svetlana Lialina
Ryan Hunt

## Slide 2
From: ITER_D_28QDBS - ITER Numbering System for Components and Parts
  Identify components and parts for ITER Project using unique identification numbers in order to make a traceability of each material throughout the ITER Project life cycle.
  ITER Numbering System for components and parts is comprised of the functional reference numbering, the ITER part number and serial number.
From: Identification Guideline for Component and Type Reference (V3EJDT v1.1) (current)
Background

## Slide 3
Blanket Parts
MANIFOLD
FLEXIBLE CARTRIDGE
INTERMODULAR PADS
SHIELD BLOCK
FIRST WALL
ELECTRICAL STRAP
CENTERING PADS
TEMPORARY
FIRST WALL

## Slide 4: Management and Quality Plan (MQP) Document

## Slide 5: ITER Part Number

## Slide 6: ITER Part Number
SHIELD BLOC
FIRST WALL
I004L8LAH
ENOVIA ID
Blanket connections
Based on the current MQP, the PNI is written in such a way : I00XXXXXX
XXXXXX being the ENOVIA unique ID of the detailed model to be manufactured, as a result and example, for the SB#04 type A (see next slide)
Prefix for all components

## Slide 7: SB & FW Variants Definition
For each PA, a list of all the variants can be found in IDM with the related ENOVIA ID: Blanket FW & SB variants
The following is an example (CN SB)

## Slide 8: Serial Number

## Slide 9: Serial Number
SHIELD BLOC
FIRST WALL
Blanket connections
There is no requirement from MQP to what concern the SN, nevertheless no component can be accepted on IO site without a clearly marked SN.

## Slide 10: Descriptive Code
Aiming to provide an identification that make sense to any reader, the blanket is requesting manufacturer to add a “descriptive code”.
This code shall be marked on the component separated from any other and can be found in the “variant table” (as per link given below):
RF FW list of variants
EU_FW_list_of_variants
CN_FW_List_of_variants
KO_SB_list_of_variants
CN_SB_list_of_variants
RF_BMC_List_Of_Variants
EU_MAN_List_of_variants
TFW list of variants

## Slide 11: Marking for components to be received in IO
As a result, each component received in the IO site should be marked with the following:
Descriptive code : as much as feasible (related to space available mainly)
PNI : Mandatory (according to IO requirement)
SN : Mandatory (free based on manufacturer)
An example is given here :

## Slide 12: Functional Reference
The FR proposed here are subject to further evolution :
TTT codes may be changed to use existing ones based on “function” of the component
Manifold may need evolution to fit with P&IDs
The Final FR may be set in a later stage as these numbers will only be needed at assembly stage and shall not impact the procurement of the blanket system.

## Slide 13: PBS Structure from Engineering Data Base

## Slide 14: Customization vs. numbering
IO (warehouse)
IO Manufacturer or DA
(Customization according to specific location in the plant)
IO (ready for installation)
DA Manufacturer
SN (unique)
PNI
SN (unique)
PNI
SN (unique)
PNI
SN (unique)
PNI
Survey / Trial Fit = definition of the needed customization

## Slide 15
16AABB-TTT-0000
Fixed PBS number: “16”
Valid TTT codes to identify function
2-letters as per PBS structure: “FW” for first walls, “SB” for shield blocks
“MA” for manifold
“NL” for neutral beam liners
“TW” for temporary first walls
2-digit number/letter as per PBS structure: Poloidal-row number for FW, SB, TW (01-18)
Subcomponent for manifold (BA, CP, CR…)
Subcomponent for liners (DL, HP)
Fixed hyphen: “-”
Functional Reference Component Number
Poloidal position (if needed) from 01 to 18
OR
Port number for manifold bundles from 01 to 18
Toroidal Position within a row:
1 to 4 on Outboard
1 or 2 on Inboard
Sector 1 to 9
OR
1 for inlet manifold
2 for outlet manifold

## Slide 16
16SBBB-TTT-0000
Fixed PBS number: “16”
Valid TTT codes to identify function
2-digit for poloidal position (01 to 18)
Fixed hyphen: “-”
Functional Reference Component Number
Sector 1 to 9
Position within a blanket 1 to 4
Toroidal Position within a row:
1 to 4 on Outboard
1 or 2 on Inboard
Specific case for Blanket Modules Connections due to missing amount of NNNN to properly locate the component (up to 4 per blanket modules)

## Slide 17: Functional Reference Component Number
Toroidal Position 2
Not needed
Not Needed
Sector 1
PPPPPP-TTT-NNNN
16FW01-TTT-1002
Example FW (same for SB)
First Wall
Poloidal row 1
Same as PBS structure
PPPPPP-TTT-NNNN
16SB12-TTT-1034
Example BMC (blanket module connection)
SB as per existing PBS structure
Poloidal position
New TTT codes to be defined
New TTT code to be defined
Toroidal position 4
Position 3 in the module (upper right)
Not needed
Sector 1

## Slide 18: TTT codes
“Within the Functional Reference the TTT Code that sets the function of the component”
As all blanket components are non-standard (such as an heat exchanger, a pump […]) the PBS structure defining this component in relation with function is proposed to be used.
Blanket Manifold (to be updated)
  Branch pipes  BBA
  Chimney pipes  BCH
  Coax reaction features  BCR
  Flanged extensions  BFE
  Inboard bundles  BIB
  Lower port pipes  BLP
  Lower port supports  BLS
  Outboard bundles  BOB
  Outboard supports  BOS
  Upper port pipes  BUP
  Upper port supports  BUS
Neutral beam port liner components
(DNB liner and HNB Plates)  NLC
For information: available TTT codes and their family description can be found in the folder
02. Function Category Designators : TTT code
Shield Blocks  SB
First Walls (First Wall for DT phases
and Temporary First Wall for SRO phase)  FW
Blanket module connection :
  1/ pads
  Centering key pads  BCP
  Intermodular key pads  BIP
  Stub key pads  BSP
  2/ Electrical straps
  Electrical strap pedestal  BEP
  Electrical straps  BES
  3/ Flexible cartridges  BFC

## Slide 19: Inboard / outboard Toroidal column Explanation

## Slide 20: Blanket inboard/outboard

## Slide 21: Blanket column
Top views
Blanket sector
VV sector
11
12
01
02
03
04

## Slide 22: Connection numbering
As modules are mounted around the poloidal profile, inboard, top and outboard modules can have different orientation, numbers should always be as per below:
1
2
1
2
Electrical strap example
Outboard module
Inboard module

## Slide 23: Blanket connections

## Slide 24: Blanket module connections
1
2
3
4
Electrical strap 1 and 2 (assembled onto SB prior to in-vessel assembly)
Electrical strap pedestal 1 and 2 (welded onto VV shell)
1
2
3
4
Outboard module
Inboard module
stub key pads (1,2,3 and 4)
Centering key pads (1 and 2)
Intermodular key pads
Flexible cartridges (1,2,3 and 4)
1
2
1
2
1
2

## Slide 25: Functional Reference Component Number
Toroidal Position 3
Position 2 in the module
Not used
Sector 1
PPPPPP-TTT-NNNN
16SB12-BES-1023
Electrical straps
Poloidal row 12
PPPPPP-TTT-NNNN
16SB08-BIP-1041
Intermodular key pads
Toroidal position 1
Position 4 in the module
Not used
Sector 1
Blanket Electrical strap
Poloidal row 08
Blanket Intermodular key pad

## Slide 26: First walls Temporary First walls

## Slide 27: Functional Reference Component Number
Toroidal Position 4
Not needed
Not Needed
Sector 6
PPPPPP-TTT-NNNN
16FW11-FW-6004
First Wall
Poloidal row 11
Same as PBS structure
Toroidal Position 4
Not needed
Not Needed
Sector 6
PPPPPP-TTT-NNNN
16TW04-FW-6004
Temporary First Wall
Poloidal row 04
Same as PBS structure
First Wall (for DT phases)
Temporary First Wall (for SRO phase)

## Slide 28: Manifolds (to be updated)

## Slide 29: Blanket Manifolds
Outboard bundle (inlet)
Chimney pipes
(inlet)
Upper port pipes
(inlet)
Branch pipe
The branch pipes are water connection for each blanket module
Positioning as per SB and FW is used (outboard/inboard/poloidal position/toroidal position)
The bundles (and pipes) are located relative to the port (1 to 18)

## Slide 30: Manifold branch pipes
SB as per existing PBS structure
Poloidal position
Manifold system
Branch pipes
PPPPPP-TTT-NNNN
16SB12-BBA-1130
Toroidal position 3
Inlet 1, Outlet 2
Sector 1
PPPPPP-TTT-NNNN
16NLDL-BBA-0100
Neutral beam port liner
Diagnostic neutral beam liner
Not needed
Not needed
Inlet 1, Outlet 2
Not needed
Not needed

## Slide 31: Chimney pipes
Manifold system
Chimney Pipes
PPPPPP-TTT-NNNN
16MACP-BCH-1123
Nozzle Number 04 to 43
Port Number 1 to 18
Pipe 41
Pipe 47
Pipe 46
Pipe 45
Pipe 43
Pipe 44
Pipe 48
Pipe 42

## Slide 32: Flange Extension
Potentially these are ‘Commercially off The Shelf’ items
Manifold System Flange Extension
PPPPPP-TTT-NNNN
16MACP-BFE-1123
Nozzle Number 04 to 43
Port Number 1 to 18

## Slide 33: Coax Reaction features
Manifold System Coax Reaction
PPPPPP-TTT-NNNN
16MACR-BCR-1073
Toroidal position 3
Poloidal position 07 or 08
Sector 1

## Slide 34: Inboard Bundles
Manifold System Inboard Bundles
PPPPPP-TTT-NNNN
16MAIB-BIB-1120
Not needed
Port 1 to 18
Inlet 1, Outlet 2

## Slide 35: Outboard Bundles & Supports
Manifold System Outboard Bundles
PPPPPP-TTT-NNNN
16MAOB-BOB-1120
Final Toroidal destination (if required)
Port 1 to 18
0 both, Inlet 1, Outlet 2
PPPPPP-TTT-NNNN
16MAOB-BOB-0043
Final Toroidal destination
Port 4 or 6
0 both, Inlet 1, Outlet 2
Detachable legs – 8 per bundle
Tandem Bundles + integral bump stops
Outboard Supports
Sliding supports not integral to Branch pipes

## Slide 36: Upper Port Pipes & Supports
Manifold System Upper Port pipes
PPPPPP-TTT-NNNN
16MAUP-BUP-1123
Nozzle Number
Port Number 1 to 18
PPPPPP-TTT-NNNN
16MAUP-BUS-1123
Port Number 1 to 18
Column 1 to 8
Row 1 to 5
10-11 upper port pipe + integral support up to Branch pipe interface

## Slide 37: Lower Port Pipes & Supports
Manifold System Lower Port pipes
PPPPPP-TTT-NNNN
16MALP-BLP-4121
Toroidal Destination (1 right and 2 left as per picture below)
Port Stub Extension 1 or Through Bulkhead 2
Inlet 1 or Outlet 2
Lower Port No 4 or 6
Manifold System Lower Port Supports
PPPPPP-TTT-NNNN
16MALP-BLS-4121
Toroidal Destination (1 right and 2 left as per picture above)
Support No. 1- 5 looking into vessel
Inlet 1 or Outlet 2
Lower Port No 4 or 6
In-vessel pipe arrays classified as Outboard Bundles
Branch pipes

## Slide 38: Neutral beam port liner components

## Slide 39: Blanket / Neutral Beam port liners
Diagnostic neutral beam liner is fixed to VV shell
Heating neutral beam plates are attached to SB prior to assembly in-vessel, it can be:
Top panel on module #16
Side panel on module #15
Bottom plates on module #14
Sector #02
Sector #03
Example of top plate #16

## Slide 40: Functional Reference Component Number
Not needed
Not needed
Not needed
Not needed
PPPPPP-TTT-NNNN
16NLDL-NLC-0000
Diagnostic neutral beam liner (only one part in the whole machine)
Neutral beam port liner
Diagnostic neutral beam liner
(Same as PBS structure)
PPPPPP-TTT-NNNN
16NLHP-NLC-2153
HNB plates
Position 3
Module 15
Sector 2
Neutral beam port liner
HNB plates
(Same as PBS structure)

## Slide 41: Shield blocks

## Slide 42: Functional Reference Component Number
Toroidal Position 2
Not needed
Not Needed
Sector 1
PPPPPP-TTT-NNNN
16SB01-SB-1002
Shield Block
Poloidal row 1
Same as PBS structure